## Slide 1
CURRICULAR DEVELOPMENT ACTIVITY
Programmatic Control of SDR Hardware
for GNSS Signal Transmission
Gabriel Matias Falcão
Bachelor in Computer Science — NOVA FCT | Initial curricular stage + continuation at GMV
March 11 — July 17, 2026

## Slide 2
CONTEXT
Why GNSS signal simulation matters
GNSS constellations
GPS, Galileo, GLONASS, BeiDou — satellites broadcasting positioning signals to receivers worldwide.
Signal simulators
Reproduce satellite signals on the ground, enabling controlled, repeatable receiver testing without waiting on real satellites.
SDR as the transmission layer
Pre-computed I/Q samples are streamed through Software-Defined Radio hardware to produce realistic RF signals.
1
GMV — SDR Control & PPP over RS-232

## Slide 3
PROBLEM
A gap between hardware and high-level intent
DTAPI is low-level
Configuring DekTec SDR hardware requires precise call sequencing, manual state management, and direct handling of FIFO/DMA details.
No bridge to open-source tools
No existing solution connects open-source GNSS I/Q generators to professional-grade SDR hardware.
RS-232 is only a physical link
The serial interface solves transport at the electrical level, but a robust high-level control path still has to be carried across it.
2
GMV — SDR Control & PPP over RS-232

## Slide 4
PROPOSED WORK
Three phases, one goal: programmatic control
Phase 1
SDR Control
C++ abstraction over the DTAPI for device management, signal transmission and synchronisation.
Phase 2
Parameter Management
A configuration system to manage SDR transmission parameters without low-level API calls.
Phase 3
RS-232 Connectivity
A serial connectivity layer for integrating external equipment and exposing the control plane across that link.
3
GMV — SDR Control & PPP over RS-232

## Slide 5
SCOPE EVOLUTION
Requirements rarely stay fixed
RS-485 to RS-232
The proposal mentioned RS-485, but the real equipment used RS-232 from the outset. This was identified early and had minimal design impact.
PPP replaced custom serial protocol
A bespoke RS-232 application protocol was dropped in favour of PPP over the serial link, so the existing gRPC control plane could run over IP unchanged.
Continuation at GMV
Some final architectural decisions were completed after the curricular stage, once the work continued directly under GMV.
4
GMV — SDR Control & PPP over RS-232

## Slide 6
SDR CONTROL SYSTEM
Client-server architecture over gRPC
CLI Client
user-facing
Server
gRPC
app + dt_facade
DTAPI wrapper
DTAPI
vendor SDK
DTA-2115B /
DTA-2116
PCIe cards
.proto contract — stub & skeleton autogenerated by protoc from the same source
Why gRPC?
Reliability & performance — proven in production systems
Strongly-typed contract between server and client
Reflection — debugging, config parsing, command discovery for free
5
GMV — SDR Control & PPP over RS-232

## Slide 7
DESIGN DECISIONS
Consistent principles across both systems
Errors as values
std::expected<T,E> instead of exceptions or C-style codes — explicit, compile-time checked error handling.
CMake build system
Easier integration with surrounding toolchains, test workflows, and packaging in a conventional C++ environment.
Reuse standard stacks
PPP over RS-232 creates an IP link, allowing the same gRPC interface to be reused instead of maintaining a second custom protocol.
6
GMV — SDR Control & PPP over RS-232

## Slide 8
SDR CONTROL DEMO
Live demonstration of the SDR control system
7
GMV — SDR Control & PPP over RS-232

## Slide 9
RS-232 INTERFACE
PPP over RS-232 carrying an IP channel
gRPC Client /
Server
IP Stack
PPP Endpoint
RS-232 Serial
Port
Core ideas
RS-232 is kept as the physical transport only
PPP creates a point-to-point IP link over the serial byte stream
The existing gRPC control plane then runs unchanged over that link
Less duplicated protocol logic, easier testing and debugging
8
GMV — SDR Control & PPP over RS-232

## Slide 10
INTEGRATION & TESTING
Validated against real hardware
External tester
Simulates the remote receiver over PPP on top of RS-232, exercising the serial link, IP transport and gRPC control path end-to-end.
Test 1 — Power configuration (Rohde & Schwarz NRQ6)
Test 2 — Frequency configuration (frequency counter)
Test 3 — Signal recording (Ettus USRP X310)
Adopted integration path
Rather than maintain a bespoke application protocol over the serial link, the final system establishes PPP over RS-232 and reuses the existing gRPC client-server interface over the resulting IP channel.
This keeps the control surface transport-agnostic: once the lower layer looks like a network link, the higher layers remain unchanged.
9
GMV — SDR Control & PPP over RS-232

## Slide 11
CHALLENGES FACED
Where the hard problems actually were
DTAPI quirks
DTAPI documentation isn't always accurate; some functions have unexpected side effects. Some don't show complete error information.
Serial driver & wiring
Generic 8250 driver was insufficient for the WCH CH382 card; replaced with the vendor driver. A missing null-modem adapter caused two DTE devices to transmit into each other's TX line.
10
GMV — SDR Control & PPP over RS-232

## Slide 12
CONCLUSION
Two systems, one consistent engineering approach
SDR Control System — a clean, remotely accessible, gRPC-based abstraction over the DTAPI.
RS-232 Interface — PPP over serial providing a standard IP channel for the same gRPC control plane.
Lesson: extensibility paid off for external, unpredictable change — but generality pursued ahead of need had a real cost.
11
GMV — SDR Control & PPP over RS-232

## Slide 13
Thank you
Questions & Discussion